## Slide 1
TEAM BRIEFING · ARCHITECTURE, PROCESSES & SOLUTION
Smart Manufacturing
Process Optimization
AI-driven predictive maintenance and workflow optimisation — from factory sensor data to a prioritised, explained action plan for the shift supervisor.
Predict
Explain
Optimise
Decide
Act
Domain: Manufacturing & Industrial IoT
Notes: Welcome. This session walks through the Smart Manufacturing Process Optimization project: the problem, how the solution is architected, how data flows through it, and what results we get. The five words at the bottom are the backbone of the whole system: Predict, Explain, Optimise, Decide, Act.

## Slide 2
AGENDA
What we'll cover
SMPO · 2
01
Problem & solution overview
Why factories lose output and our 5-stage answer
02
Datasets
AI4I 2020 + Azure PdM, and why
03
Architecture & request flow
Layers, agent run sequence, factory replay
04
Data pipeline & ML models
Features, LightGBM, anomaly detection, results
05
Optimisation & business case
Setpoints, CP-SAT scheduling, OEE
06
Decision agents (LLM layer)
Agents, tools, backends, modes, safeguards
07
Dashboard & operations
7 pages, setup, config, testing
08
Design decisions & roadmap
Trade-offs, limitations, next steps
Notes: Eight sections. We'll go from the business problem down into architecture and models, then back up to business value, operations and the roadmap.

## Slide 3
01 · PROBLEM
Factories lose output to three linked problems
SMPO · 3
Machine downtime
SYMPTOM
Components fail without warning. An unplanned repair stops a machine for 24 h vs 4 h for a planned one.
WHAT WE DO
Predict component failures 24 h and 7 days ahead; flag abnormal sensor behaviour.
Quality losses
SYMPTOM
Cycles fail through heat build-up, power overload, overstrain or tool wear.
WHAT WE DO
Predict cycle failure and its mode, explain the physical cause, find safer setpoints.
Reactive workflows
SYMPTOM
Maintenance is reactive or calendar-based — ignoring risk, crew capacity and production load.
WHAT WE DO
Schedule maintenance to minimise expected cost under crew and load constraints.
Notes: Three problems that feed each other: downtime, quality losses and reactive maintenance. The key number is 24 hours of downtime for an unplanned failure versus 4 hours when planned. Every capability in the system maps to one of these three columns.

## Slide 4
02 · SOLUTION OVERVIEW
From sensor data to action in five stages
SMPO · 4
1
Predict
LightGBM + Isolation Forest: component failures (24 h, 7 d), cycle failures & modes
›
2
Explain
SHAP feature contributions + known physical failure rules
›
3
Optimise
Model-verified setpoint search; OR-Tools CP-SAT weekly maintenance plan
›
4
Decide
LLM agents call models as tools → structured, prioritised action plan
›
5
Act
Dashboard: accept / reject every recommendation; every decision logged
Core principle: the LLM never predicts failures.
Trained models, optimiser and scheduler are the source of truth. The LLM interprets their output, connects evidence and communicates the decision. Setpoint recommendations are re-scored by the failure model before they are shown.
Notes: The pipeline: predict, explain, optimise, decide, act. Agents run on a free local model via Ollama or on Claude. The most important design principle: the LLM is a decision and communication layer, not a predictor. Numbers always come from measurable, testable models.

## Slide 5
03 · DATASETS
Two complementary public datasets
SMPO · 5
 | AI4I 2020 (UCI #601) | Microsoft Azure PdM
Scope | Machining line, one row per production cycle | 100 machines, hourly, calendar year 2015
Size | 10,000 cycles, 3.39% failures | 876,100 telemetry rows · 3,919 errors · 3,286 replacements · 761 failures
Signals | Air/process temp, speed, torque, tool wear, quality variant L/M/H | Voltage, rotation, pressure, vibration; error codes; model & age
Labels | Failure + modes: TWF, HDF, PWF, OSF, RNF | Failure time per component (comp1–comp4)
Used for | Process risk, failure-mode diagnosis, setpoint optimisation, quality KPI | Fleet health, component forecasts, anomalies, maintenance planning, availability
Evaluated, not used
NASA C-MAPSS
Turbofan engines, not factory machines
SECOM (UCI)
Quality only; 590 anonymised sensors
Bosch Production Line
~14 GB, anonymised, not explainable
Both are synthetic (real physics / real plant patterns) — expect lower scores on real plant data.
Notes: AI4I explains WHY a cycle fails — failure modes map to physics, so predictions translate into process fixes. Azure gives the fleet time series with errors, maintenance and failures that we need for downtime, scheduling and OEE. Other datasets were rejected for domain mismatch, lack of explainability or size. Caveat: both are synthetic.

## Slide 6
04 · ARCHITECTURE
Layered architecture
SMPO · 6
Data layer
src/data
download.py
UCI + GitHub mirror
features.py
physics features, rolling stats, error counts, component age, labels
ML layer
src/models
train.py
LightGBM, Isolation Forest
predictor.py
ProcessModel, FleetModel, SHAP
Optimisation
src/optimization
process_optimizer.py
what-if + setpoint search
scheduler.py
CP-SAT maintenance plan
kpis.py
OEE + business case
Agent layer
src/agents
tools.py
7 strict tools
orchestrator.py
agent modes, rule-based fallback
runners
Claude · ollama_runner.py
Presentation
app/
Streamlit
dashboard, 7 pages
decisions.jsonl
accept / reject log
Simulation src/simulation/stream.py — FactoryState replays held-out data → feeds agent tools
Models, optimiser and KPIs also feed the dashboard directly — the UI works even with no LLM.
Notes: Five layers, each a Python package. Data produces features; ML trains LightGBM and Isolation Forest models and wraps them in ProcessModel and FleetModel with SHAP. The optimisation layer turns predictions into setpoints, a maintenance plan and KPIs. The agent layer exposes all of that as seven strict tools to an orchestrator that can run Claude or Ollama, with a rule-based fallback. The simulation replays held-out data as a live factory. Streamlit sits on top.

## Slide 7
04 · ARCHITECTURE
Request flow for an agent run
SMPO · 7
Supervisor
(dashboard)
Orchestrator
ToolBox
Models / optimiser
/ scheduler
LLM
(Ollama or Claude)
1 Run agent analysis (current factory time)
2 Gather evidence / tool calls
3 Snapshot, diagnose, optimise, schedule
4 Probabilities, SHAP, candidates, plan
5 Compact JSON
6 Evidence + role prompt
7 Report / structured plan (JSON schema)
8 Action plan + reasoning trace
9 Accept / reject each action → data/decisions.jsonl
Notes: One agent run end to end. The supervisor triggers analysis for the current factory time. The orchestrator gathers evidence through the ToolBox, which calls models, optimiser and scheduler and returns compact JSON. Only then is the LLM called, with evidence plus a role prompt, and it returns a JSON-schema-constrained plan. The supervisor accepts or rejects every action and that decision is logged.

## Slide 8
04 · ARCHITECTURE
Factory simulation: replaying held-out data
SMPO · 8
Fleet clock
Azure test period (1 Sep 2015 onwards) advanced in 3-hour steps across 100 machines.
Machining line
AI4I 20% test cycles — including every failing cycle — replayed as the production line.
No look-ahead
Models & agents see only the state at the current clock position
Actual future failures appear only in a “ground truth” expander for demo evaluation
Ground truth is never passed to the agents
Sidebar controls
Factory clock slider · +3 h · +1 day · production-cycle picker · active decision engine (Ollama / Claude / rule-based).
Notes: The dashboard treats held-out test data as a live factory. The fleet clock walks through the Azure test period in 3-hour steps; the machining line replays the AI4I test cycles. This means the demo is honest: nothing the agents see comes from the future.

## Slide 9
05 · DATA PIPELINE
Three commands from raw data to trained models
SMPO · 9
python -m src.data.download
→ data/raw/*.csv (~80 MB)
›
python -m src.data.features
→ ai4i / azure_features.parquet (~10 s)
›
python -m src.models.train
→ models/*.joblib, reports/metrics.json (~1 min)
AI4I features — per production cycle
temp_diff_k: process − air temp (HDF when < 8.6 K at low speed)
power_w: torque × rpm × 2π/60 (PWF outside 3,500–9,000 W)
strain_minnm: tool wear × torque (OSF > 11k/12k/13k for L/M/H)
strain_ratio, type_code, raw setpoints
Physics-rule flags → hard, explainable evidence; covers tool wear (flag from 190 min)
Azure features — per machine, every 3 h
Telemetry: volt, rotate, pressure, vibration + 3 h / 24 h rolling mean & std
Errors: count of error1–error5 in the last 24 h
Component age: days since last replacement (strictly before t — no leakage)
Machine: model, age
Labels: component fails within 24 h / 7 days (strictly after t)
292,100
rows × 41 columns
Notes: The pipeline is three commands. On the AI4I side we engineer physics features that mirror the documented failure rules, and we also implement those rules as explicit flags. On the Azure side we build rolling telemetry statistics, error counts and component ages, with careful handling of time to avoid leakage.

## Slide 10
06 · PREDICTIVE MODELS
Seven model families, all explainable
SMPO · 10
Model | Algorithm | Output
Machine failure (process) | LightGBM | P(cycle fails); alert threshold tuned on out-of-fold predictions
Failure mode × 4 (TWF, HDF, PWF, OSF) | LightGBM | P(each mode)
Component failure within 24 h × 4 | LightGBM | P(comp fails in 24 h) → drives urgent alerts
Component failure within 7 days × 4 | LightGBM | P(comp fails in 7 d) → drives weekly scheduling
Anomaly detector | Isolation Forest (24 h telemetry stats) | Score: 0 = typical, > 1 = beyond 99th pct of normal
Explanations | SHAP TreeExplainer | Per-prediction feature contributions (log-odds)
No class re-weighting: keeps probabilities calibrated for cost calculations; class imbalance is handled by tuning the alert threshold instead.
Notes: All supervised models are LightGBM. We deliberately avoid class re-weighting because the scheduler uses the probabilities in cost formulas, so they must be calibrated. An Isolation Forest flags abnormal telemetry, and SHAP explains every prediction.

## Slide 11
06 · PREDICTIVE MODELS
Held-out evaluation results
SMPO · 11
Chart: Machining line (AI4I) — PR-AUC, 80/20 split
| Machine failure | Heat dissipation | Power | Overstrain | Tool wear
PR-AUC | 0.891 | 1 | 0.982 | 0.971 | 0.061
0.996–1.000
PR-AUC, 24 h component models
Near-perfect: synthetic data has strong pre-failure signals
~10×
better than base rate, 7-day models
PR-AUC 0.35–0.52 vs 2.4–4.9% base rate — enough to rank for weekly planning
11.4% vs 1.0%
anomaly flags before failures vs overall
Readings flagged in the 24 h before a failure
Tool wear is random between 200–240 min — unpredictable from one cycle. The physics rule covers it. Fleet: time split, train Jan–Aug 2015, test Sep onwards.
Notes: Machine-failure model: PR-AUC 0.891, precision 0.949, recall 0.824 at threshold 0.47. HDF, PWF and OSF are nearly perfect because they follow deterministic physics. Tool wear is effectively random and no model can predict it, which is exactly why we keep the physics rules. On the fleet, 24-hour models are near perfect (synthetic data), and 7-day models are about ten times better than the base rate — good for ranking.

## Slide 12
07 · OPTIMISATION
Process setpoint optimiser
SMPO · 12
Search space
Speed −15% to +25%, torque −30% to +50% (5% steps), optional tool change; kept within the training range
Constraint
Speed ≥ min_throughput_ratio × current speed (default 0.9) — speed is the throughput proxy
Objective
Failure prob. + 0.5 × throughput loss + small change-size penalty + tool-change penalty → smallest fix that works
Verification
Every candidate scored by the trained failure model; simulate() re-scores any what-if
67 / 68
failing test cycles brought below 20% risk
EXAMPLE — HEAT-DISSIPATION FAILURE
Speed 1363 → 1431 rpm (+5%)
99.9% → 0.01%
Moves speed above the 1380 rpm heat-dissipation limit.
Notes: The setpoint optimiser is a model-verified search. It enumerates speed and torque adjustments within the range seen in training, keeps throughput above 90%, and prefers the smallest change that fixes the risk. Every candidate is re-scored by the failure model, so nothing is recommended without a predicted risk reduction. It fixes 67 of 68 failing test cycles.

## Slide 13
07 · OPTIMISATION
Maintenance scheduler (OR-Tools CP-SAT)
SMPO · 13
Jobs: every (machine, component) with 24 h or 7-day risk ≥ 5%
Decision: replace on day d of the horizon, or don't schedule
Cost of replacing on day d: planned cost + planned downtime × day's load + P(fails before d) × unplanned cost
Cost of not scheduling: P(fails within horizon) × unplanned cost
Constraint: at most crew_per_day jobs per day
FAILURE TIMING
P(fail < d) = 1 − (1 − p24h)(1 − h)^(d−1)
h = constant daily hazard implied by the 7-day probability
Chart: Expected cost, week of 26 Sep 2015
| Optimised plan | Run-to-failure
Expected cost | 187.6 | 326.8
$139,174 expected saving that week
Notes: The scheduler turns probabilities into a plan. For every at-risk component it decides whether and on which day to replace, trading planned cost and downtime weighted by production load against the risk of failing before that day, subject to crew capacity. On the 26 September example it schedules 14 jobs and cuts expected cost from about 327k to 188k dollars.

## Slide 14
07 · OPTIMISATION
OEE and the business case
SMPO · 14
Availability
96.9%
Azure downtime over 100 machine-years
Performance
99.3%
Mean rotation vs 450 rpm nominal
Quality
96.6%
AI4I cycles without failure
OEE today
92.9%
Availability × Performance × Quality
WITH PREDICTIVE MAINTENANCE (24 h models detect 99.7% of failures; 70% converted to planned work)
531
failures prevented / yr
10,623 h
downtime saved / yr
~$14.1M
saved per year
94.1%
OEE (from 92.9%)
All costs and downtime hours are assumptions in src/config.py — edit them for your plant.
Notes: OEE is 92.9% today. With predictive maintenance, assuming 70% of detected failures become planned work, we project 531 failures prevented, over 10,000 downtime hours saved and about 14 million dollars a year, lifting OEE to 94.1%. Stress that these rely on configurable cost assumptions.

## Slide 15
08 · DECISION AGENTS
Six agents, seven strict tools
SMPO · 15
Monitoring
get_fleet_overview, get_machine_details
Prioritised watch-list
Diagnosis
get_process_status, get_fleet_overview, get_machine_details
Failure mode → mechanism → evidence
Maintenance planning
plan_maintenance, get_fleet_overview, get_plant_kpis
Day-by-day plan, cost vs run-to-failure
Process optimisation
get_process_status, optimize_process_setpoints, simulate_process_change
Verified setpoint change
Coordinator
none — JSON-schema output
De-duplicated, prioritised action plan
Chat assistant
all 7 tools
Answers questions, runs what-ifs
Tools return compact JSON with strict schemas; unknown args are dropped; tool errors go back to the model instead of crashing. Plan schema: headline, situation_summary, actions[] (priority, category, urgency, target, action, rationale, expected_impact, source_agents), risks_and_caveats[].
Notes: Four specialists — monitoring, diagnosis, maintenance planning and process optimisation — each have a narrow tool set. A coordinator merges their reports into one de-duplicated plan using a JSON schema. A chat assistant has access to all seven tools for ad-hoc questions and what-ifs.

## Slide 16
08 · DECISION AGENTS
Pluggable LLM backends and agent modes
SMPO · 16
 | ollama (default) | claude
Model | qwen3:4b | claude-opus-5-5
Cost | Free, offline, no token limits | Pay per token
Setup | ollama pull qwen3:4b | ANTHROPIC_API_KEY
Default mode | narrate | tools (parallel)
Mode | What the LLM does | Calls | CPU time*
tools | Specialists choose & call own tools; coordinator merges | 10–30 | > 10 min / call
evidence | Code runs tools; LLM writes 4 reports + merged plan | 5 | ~8 min / report
compact | Code runs all tools; LLM writes whole plan | 1 | 612 s
narrate | Models build actions; LLM writes headline, summary, caveats | 1 | 86 s ✓
* qwen3:4b on Intel i5-1135G7, no GPU, 20 GB RAM
Why narrate is the CPU default
On CPU the model reads ~30–36 tokens/s and generates ~2–8 tokens/s, slowing as context grows. narrate keeps the prompt near 1k tokens and output near 200. On a GPU or with Claude, use compact or tools. llama3.2 (3B) was rejected: it claimed a what-if simulation it never ran — so lighter modes run tools in code.
Notes: The LLM backend is pluggable: free local Ollama or Claude, sharing the same tools and plan schema. Agent modes trade LLM autonomy for speed. On a laptop CPU only narrate is practical, at about a minute and a half. Cursor was considered but has no public API for calling its models.

## Slide 17
08 · DECISION AGENTS
Reliability safeguards
SMPO · 17
Grounding
Every prompt requires numbers to come from tool results; lighter modes run the tools (incl. what-if verification) in code.
Structured output
Plans generated against a JSON schema; Ollama output validated with jsonschema and retried once.
Graceful fallback
No credits, Ollama down, timeout → deterministic rule-based planner; dashboard shows why.
Append-only history
Chat turns appended; a failed turn is rolled back so history stays valid.
Claude-specific
Server-side refusal fallback; refusal / max_tokens / pause_turn handling; typed error mapping.
Human in the loop
Supervisor accepts or rejects every action; logged to data/decisions.jsonl.
Notes: Six safeguards make the LLM layer production-minded: grounding in tool output, schema-validated output, a rule-based fallback so the dashboard works without any LLM, consistent chat history, Claude-specific error handling, and a human who approves every action.

## Slide 18
09 · DASHBOARD
Streamlit dashboard — seven pages
SMPO · 18
Fleet overview
KPI tiles, OEE ± PdM, 7-day risk heatmap, business case, watch-list
Machine health
Component risk, SHAP drivers, 14-day telemetry, errors, replacements
Process optimizer
Diagnosis, mode probabilities, physics flags, candidates, what-if
Maintenance plan
Horizon & crew sliders, crew load vs capacity, cost vs run-to-failure
Agent action plan
Run agents; prioritised actions with accept/reject; reasoning trace
Assistant
Chat with tool access; suggested questions; tool-call trace
Model performance
All evaluation metrics
streamlit run app/streamlit_app.py
Opens at http://localhost:8501 (use port 8502 if busy)
Notes: Seven pages, from fleet-level KPIs down to a single machine or production cycle, plus the agent action plan, a chat assistant and a model-performance page. The sidebar holds the factory clock, cycle picker and decision engine selector.

## Slide 19
10 · SETUP & CONFIGURATION
Running it and tuning it
SMPO · 19
pip install -r requirements.txt
cp .env.example .env
ollama pull qwen3:4b
python -m src.data.download
python -m src.data.features
python -m src.models.train
streamlit run app/streamlit_app.py
Python 3.11+ · ~1 GB disk · Ollama with ~4 GB free RAM. For Claude: LLM_PROVIDER=claude + ANTHROPIC_API_KEY.
.env | Default
LLM_PROVIDER | ollama
AGENT_MODE | narrate / tools
OLLAMA_MODEL | qwen3:4b
OLLAMA_NUM_CTX | 8192
CLAUDE_EFFORT | medium
Business assumptions (src/config.py)
Unplanned failure $12,000 · planned $1,500 · downtime $800/h
Downtime: unplanned 24 h · planned 4 h
Crew 4 jobs/day · horizon 7 days · nominal 450 rpm
Daily load 1.0, 1.2, 1.2, 1.0, 0.8, 0.5, 0.4 · PdM realisation 0.7
Notes: Setup is a handful of commands. Configuration splits into .env for the LLM backend and src/config.py for business assumptions. Changing the cost and load assumptions changes the scheduler and business case, so plant teams should review them.

## Slide 20
11 · QUALITY & CODE
Testing and project layout
SMPO · 20
32
pytest tests — no network, API or LLM calls (clients mocked)
test_features.py
Derived features and each physics rule
test_optimization.py
Failure timing, scheduler capacity & urgency, optimiser fixes an HDF failure
test_agents.py
Tool schemas, Claude/Ollama loops, JSON retry, modes, fallback, chat rollback
test_app.py
Every dashboard page renders headlessly (AppTest)
SMPO/
+- src/
| +- config.py
| +- data/ download, features
| +- models/ train, predictor
| +- optimization/ optimizer, scheduler,
| | kpis
| +- simulation/ stream.py
| +- agents/ tools, prompts,
| orchestrator, ollama_runner
+- app/ streamlit_app, pages
+- notebooks/ 01_eda.ipynb
+- tests/
+- data/, models/ (generated)
+- reports/metrics.json
Notes: 32 tests run offline with mocked LLM clients, covering features, optimisation, the agent loops including failure paths, and headless rendering of every dashboard page. The code layout mirrors the architecture layers one to one.

## Slide 21
12 · DESIGN DECISIONS
Key trade-offs we made
SMPO · 21
Two datasets
AI4I explains why a cycle fails; Azure gives fleet time series and maintenance history
LLM as decision layer, not predictor
Predictions stay measurable and testable
LightGBM without re-weighting
Calibrated probabilities for cost maths; tune the threshold instead
Time-based split for the fleet
Test months lie in the future — no look-ahead
7-day classifier, not days-to-failure
Regressor barely beat the median (MAE 15 days)
Physics rules alongside ML
Covers unpredictable tool wear; hard evidence for explanations
Optimiser verifies with the model
No recommendation without a predicted risk reduction
CP-SAT scheduling
Exact risk vs load vs crew optimisation in < 1 s
Pluggable LLM + rule-based fallback
Free local or stronger Claude; dashboard works with no LLM
Notes: These are the decisions most worth defending in a review. The common thread: keep numbers in measurable models, keep the LLM for reasoning and communication, and make sure the system degrades gracefully.

## Slide 22
13 · ROADMAP
Limitations and next steps
SMPO · 22
Limitations
Both datasets synthetic — real 24 h scores will be lower
Datasets describe different plants; joined at decision layer only
Cost, downtime and load figures are assumptions
Scheduler double-charges downtime for same-machine, same-day jobs
Small local models can misstate facts in prose
No authentication; decisions logged to a local file
Next steps
Connect a real source (OPC UA / MQTT historian) in place of replay
Calibrate 7-day probabilities (isotonic); retrain on real history
Group same-machine jobs into a single stop
Feed accept/reject decisions back into scheduling & prompts
Run agents on GPU or Claude with compact / tools mode
Add sign-in (st.login) and a database for the decision log
Notes: Be candid about limitations: synthetic data, assumed costs, and no auth yet. The roadmap addresses each one — real plant connectivity, calibration, scheduler grouping, closing the feedback loop from supervisor decisions, stronger LLM modes, and production hardening.

## Slide 23
KEY TAKEAWAYS
Models are the source of truth
LightGBM, Isolation Forest, SHAP and physics rules produce every number.
Optimisation turns risk into action
Verified setpoints and a CP-SAT plan — ~$139k saved in a sample week.
LLM explains, humans decide
Grounded agents, schema output, rule-based fallback, full decision log.
Questions & discussion
Notes: Recap the three takeaways, then open the floor. Good discussion prompts: which real data source should we connect first, and who owns the business-cost assumptions?